ATTACHMENT 13

STERILIZATION AREA

STERILIZATION AREA

Introduction

Sterilization of all instruments and consumable supplies is done prior to performance in the laboratory or clinical setting. Students are instructed to sterilize all instruments and consumable supplies in a sealed bag according to the tray set-up used for clinical experience. Students will set up a minimum of four tray set-ups when working on the clinical patient experiences. These trays will be disinfected between each patient. After treatment, all instruments are transported back to sterilization area and the process of sterilization will be repeated as described in the handout.

The sterilization area contains the following equipment and supplies:

| Description: Contaminated Side of Sterilization Area | Quantity |
| --- | --- |
| Ultrasonic unit with chemical | 1 |
| Disinfectant tray with immersion disinfectant solution | 1 |
| Utility gloves | 1 pair per student |
| Holding container for enzymatic solution | 1 |
| Biohazard waste container | 6 |
| Regular trash container | 6 |
| Biohazard bag | 1 at a time |
| Trash bag | 1 at a time |
| Self sealing bags for sterilization | 100 |
| Process integrator strips, | 100 |

Instrument recirculation occurs in the sterilization area. There is a clean and contaminated area that is separated clearly defined. The sterilization area is centrally located in order to provide easy access from the treatment rooms/operatories. It is not part of the laboratory area or near the staff lounge. No eating, smoking, drinking, applying cosmetics or lip balm, or handling contact lenses occurs in this area.

Contaminated Side of Sterilization Area

The contaminated instruments and tray are placed on the counter on the contaminated side in preparation for sterilization. The contaminated area contains protective eyewear, utility gloves, counter space, a sink, a large biohazard waste container, holding solution, 1 ultrasonic unit, supplies for packaging instruments before sterilization. Prior to handling contaminated items, utility gloves are donned. All cotton products, etching/bonding materials, small biohazard bag from operatory, etc. are removed from tray and placed into large red biohazard bag. The biohazard bag is sealed and discarded into the large red biohazard waste container located on the contaminated side of the sterilization area. The instruments are placed into the ultrasonic unit. After the instruments have been removed, rinsed, and dried they are bagged for sterilization. The tray is rinsed and surface disinfected. After all the contaminated instruments, are prepared for sterilization the counters in this area are disinfected.

| Description: Clean Side of Sterilization Area | Quantity |
| --- | --- |
| Sterilizers-Autoclaves | Midmark 11 Steam Autoclave Statim 2000 Steam Autoclave |
| Nitrile gloves | 1 pair per student |
| Sterilization indicator strips | 100 |

Clean Side of Sterilization Area

The sterilizer is located on the clean side of the sterilization area. The clean area has counter space and storage drawer/space for sterilized instruments. Replacement cotton products and bonding materials are placed in the clean area in preparation for restocking the tray. Contaminated trays, instruments, and consumable products are never placed in this area.

EXPOSURE CONTROL PLAN

Impression preparation and disinfection

All intra-oral items such as impressions and bite registrations shall be cleaned and disinfected in the Dental Treatment Room with an intermediate level of disinfectant before manipulation in the laboratory.

After an impression or bite registration is completed, it needs to be disinfected properly utilizing a disinfecting solution, gloves and personal protective equipment.  This is accomplished by following the specific steps for a spray or immersion technique.

Armamentarium:

- Personal protective Equipment (PPE)

- Disinfection Solution - approved for use as hospital chemical germicide

- Airtight plastic bag

- Utility Gloves

- Paper towels

Rinse and disinfect impressions and bite registrations before transfer to the laboratory avoiding cross contamination.

Procedure:

- Use individual instrument tray set-ups whenever possible.

- Unit dose concept:  dispense enough impression material for the individual patient to avoid contamination.

- Thoroughly rinse the impression/bite registration under running tap water.

- Remove any remaining blood with camel paintbrush, soap and water.

- Spray or immerse entire impression/bite registration in disinfectant following manufacturer’s directions.

- Place sprayed/immersed impression or registration into a labeled airtight plastic bag.

- Follow manufacturer’s instructions for exposure time.

Transfer to the Laboratory

- Remove impression from plastic bag, thoroughly debride and rinse under running water prior to pouring.

- Gently shake impression/registration to remove excess water.

- When preparing slurry water, use set stone which has not been poured against an impression.

- Soak reusable impression trays in presoak for designated time, scrub in soapy water, rinse, dry, and seal in peal packs for autoclaving.

EXPOSURE CONTROL PLAN

Appliance Disinfection and transfer to the orthodontic laboratory

The key to preventing micro-organism transfer in the dental laboratory is by breaking the chain of infection or cross-contamination at critical exchange points.

All intra-oral orthodontic appliances shall be cleaned and disinfected in the Dental Treatment Room with an intermediate level of disinfectant before transfer and manipulation in the laboratory.

Armamentarium:

- Personal protective Equipment (PPE)

- Disinfection Solution - approved for use as hospital chemical germicide

- Airtight plastic bag

- Utility Gloves

- Paper towels

Rinse and disinfect appliances before transfer to the laboratory avoiding cross contamination.

Procedure:

- Use individual instrument tray set-ups whenever possible.

- Thoroughly rinse the appliance under running tap water.

- Remove any debris from appliance surface with scrub brush with soap and water.

- Store scrub brush in an approved hospital chemical germicide changed weekly or by manufacturer’s recommendations between uses and autoclave brushes weekly.

- After cleaning, place appliances in a beaker or container of disinfectant and ultrasonically clean for 10 minutes with cover in place.

- Follow manufacturer’s instructions for exposure time.

- Remove container and appliance from ultrasonic and wash with soap and water.

- Rinse appliance under running water to eliminate residual disinfectant.

- Gently shake appliance to remove excess water.

Outgoing Appliance preparation, packaging, and delivery

After an appliance is fabricated in the laboratory, it needs to be disinfected properly prior to delivery to the patient.

Procedure:

- Thoroughly rinse the appliance under running tap water.

- Remove any debris from appliance surface with scrub brush with soap and water.

- Store scrub brush in an approved hospital chemical germicide changed weekly or by manufacturer’s recommendations between uses and autoclave brushes weekly.

- After cleaning, place appliances in an approved intermediate level disinfectant.

- Follow manufacturer’s instructions for exposure time.

- Remove appliances from disinfectant, rinse, and store in a sealed plastic bag to prevent contamination from handling.

ATTACHMENT 15

FACULTY/STUDENT RATIOS

CLASS SESSIONS/HOURS

Faculty/Student Ratios

Laboratory instruction: 		1 for every 14 students

Pre-clinical instruction: 		1 for every 6 students

Clinical instruction: 		1 for every 6 students

| Maximum Students enrolled per session: | 4 | Number of Operatories: 6 |  |
| --- | --- | --- | --- |
| Faculty/Student Ratios | Didactic: 1:4 | Laboratory/Preclinical: 1:4 | Clinical: 1:4 |

| Class Session* | Hours ** | Total Number of Students | Total Number of Faculty Providing Instruction (including Course Director) | Names of Faculty Providing Instruction (including Course Director) |
| --- | --- | --- | --- | --- |
| Monday | 4 Hours | 4 | 1 (Course Director) | Michael H. Payne |
| Tuesday | 4 Hours | 4 | “ | “ |
| Wednesday | 4 Hours | 4 | “ | “ |
| Thursday | 4 Hours | 4 | “ | “ |

* Class Session – describe the day or days the class (es) meet (s). i.e. Monday and Wednesday evenings.

** Hours – provide the hours per day(s)

ATTACHMENT 16

DESCRIPTION OF FACILITY

FLOOR PLAN

LECTURE AREA- enclosed office with seating for 6 and large screen monitor and dedicated computer for PowerPoint presentations.  Desk area available for study materials.

LAB ACTIVIES TYPODONT EXPERIENCE

Laboratory activities completed in two areas.  Laboratory facility consists of 10 foot bench with available bench mount for typodonts.  Mounting plates also available for typodont mounts at individual dental chairs with over patient and side unit delivery for instrument placement.  HVAC, air water syringe, Low speed hand piece, task lighting present. Operator chairs as each unit and in dental laboratory.

DENTAL OPERATORIES open bay consisting of 6 chairs with side units with dedicated work surface.  Each unit has task lighting, Air Water syringe, HVAC, Low speed hand piece, operator chair, and fully functioning dental chair.

STERILIZATION- L shaped area with contaminated and clean area with clear demarcation and separation of two areas.  Contaminated instrument preparation area for processing of instrument trays, biohazard waste container, ultrasonic unit, chemical immersion unit and dedicated sink with faucet and spray nozzle, two sterilizers placed in clean area.  Instrument storage in clean area and central dedicated unit.

ATTACHMENT 17

EQUIPMENT AND ARMAMENTARIUM

EQUIPMENT-SUPPLIES PROVIDED BY FACILITY

AUDIO-VISUAL EQUIPMENT & CLASSROOM INSTRUCTIONAL MATERIALS

| Description | Quantity |
| --- | --- |
| White board | 1 |
| Monitor | 1 |
| Syllabus | 1 each per module |
| Samples of typodont with ideal bonded brackets; insufficient bonding material; excess bonding material, a long with examples to include all procedures for OAP | 4 of each |
| Typodont | 1 per student |
| Bench mount | 1 per student |

DENTAL OPERATORY EQUIPMENT

| Description | Quantity |
| --- | --- |
| Dental unit | 6 |
| Dental chair | 6 |
| Dental operatory light, chair mounted | 6 |
| Operator stools | 6 |
| Side unit cabinet each chair; sink, glove, cup dispenser | 6 |
| Hand washing sinks in Central Cabinet | 3 |
| Handpiece, slow speed | 6 |
| Handpiece high speed (DDS use only) | 6 |
| Eyewash faucet | 2 |
| Hand-wash sink-between two operatories | 3 |
| Dental X-ray machine | 1 |
| Ultrasonic Scaler Unit (removal of cement from tooth) | 6 |

STERILIZATION AREA

| Description | Quantity |
| --- | --- |
| Sterilizer, Autoclave | 2 |
| Ultrasonic unit (for instrument reprocessing) | 1 |
| Instrument transfer forceps | 2 |
| Nitrile utility gloves | 1 pair per student |
| Holding Container (bagged un-sterilized instruments) | 1 |
| Biohazard waste containers with bags | 6 |
| Regular trash container with bags | 6 |
| Safety glasses for patients/students | 1 per patient/student |

INFECTION CONTROL SUPPLIES

| Description | Quantity |
| --- | --- |
| Immersion disinfectant | 1 gallon |
| Concentrated surface disinfectant | 1 bottle |
| Spray or bottles with spout | 6 |
| Sterilization bags of varying size | 2 |
| Masks, disposable | 6 boxes |
| Barriers, chair | 1 roll |
| Barriers, hoses, unit, light switches, etc. | 50 of each |
| Gloves | 6 boxes of each size |
| Safety glasses | 1 pair per student |
| Nonlatex gloves | 4 boxes of each size |
| Over-gloves | 2 boxes |
| Indicator strips | 1 pkg. of 250 |
| Biohazard waste bags, large and small | 1 box each of 100 |
| Small white bags | 100 |
| Ultrasonic cleaner | 1 gallon |
| Oral evacuation cleaner | 1 gallon |
| Soap, microbial/and or hand sanitizer | 1 of /or for every sink |

BONDING CONSUMABLE SUPPLIES

| Description | Quantity |
| --- | --- |
| Bonding primer | 10 |
| Brushes/applicators for primer application | Pkg. of 100 |
| Etchant material (syringe) | 20 |
| Disposable tips for bonding materials | 100 |
| Brushes for bonding application | 100 |
| Bonding agent | 5 |
| Bonding material in syringes | 10 |
| Disposable prophy angles | 100 |
| Specialized etchants/primers for bonding | 1 of each |
| Liquid wells if necessary for dispensing agents/syringe not avail. | 100 |

OTHER EQUIPMENT AND SUPPLIES

| Tongue guard/saliva ejector assembly | 100 |
| --- | --- |
| Saliva ejectors, disposable | 100 |
| Short and long cotton rolls | 100 |
| Dri-angles | 100 |
| Air water syringe tips (3 way), disposable | 100 |
| High volume evacuation tips, disposable | 100 |
| Mouth mirror | 12 |
| Cotton pliers | 12 |
| Explorers | 12 |
| Scalers (Cement removal) | 12 |
| Orthodontic pliers | Assortment of pkgs. |
| Separating Pliers | 6 |
| Band Pusher | 12 |
| Bite Stick | 12 |
| Mechanical band seater (thumper and tip) | 6 |
| Scaler and serrated plugger | 6 |
| Crown and bridge scissors | 6 |
| Band Crimping pliers | 6 |
| Brackets | Assortment |
| Orthodontic Bands and attachments | Assortment |
| Band/bracket removing pliers | 6 each |
| Arch Wires | Assortment |
| Ligation materials | Assortment |
| Archwire placement and adjustments kits | Assortment |
| 2 X 2 gauze | 12 |
| Plastic tray for instrument set up or cassettes | 6 pkgs. |
| Paper tray covers for plastic trays | 1 case |
| Cups, small | 100 |
| Neck chain/bib clip | 2 per operatory |
| Slow speed hand piece with Midwest attachment | 2 per operatory |
| Prophy angles, disposable | 1 case |
| High speed drill (used only by orthodontist when indicated) | 1 per patient |
| Burs for high speed hand piece (variety) | 1 each per patient |
| Curing Light with shield | 1 per operatory |
| Pumice without oil or fluoride in disposable cups | 1 case |
| Pumice/prophy paste (after bracket/band removal) |  |
| Utility gloves for operatory maintenance | 1 pair per student |
| Masks | New for each patient |
| Gloves | New for each patient |
| Protective eyewear | 1 pair per student |
| Gown/outer garment over scrubs | 1 per student |
| Scrubs | 1 set per student |

ATTACHMENT 19

DESCRIPTION OF OPERATORIES

Examination Room

Dental Chair

Operator Stool

Side Unit with task lighting, Air Water syringe, HVE, Low speed and high-speed hand piece

Main Operatory

6 dental Chairs

6 operator stools

6 side units Side Unit with task lighting, Air Water syringe, HVE, Low speed and high-speed hand piece

Overhead task lighting

Central Unit with 3 sinks